RTL Design
Copyright 2014, Ecancello Systems, Inc. - Phone : 512 925-2983 – email:sales@ecancello.com

---
RTL Definition
Register Transfer Level (RTL) is the defining of logic paths from one synchronous register to the next in the form of a Hardware Description Language (HDL)
HDL Languages include Verilog and VHDL
This presentation uses Verilog as the HDL language
One needs to first understand the details of the synchronous register to grasp the details of HDL
A register or Flip Flop is the smallest form of data storage in a digital logic device
A single logic bit of data, a 1 or a 0, is stored in the synchronous register at the rising edge of a clock
Where a clock is a constantly toggling signal at a specific rate or frequency
The most basic form of a register is the following
D – Data input
C – Clock input
R or S – An asynchronous reset or set input to put the register into a know state at a power up event
Q/Qn – Output value that is the captured value of the D input at the rising edge of the clock signal

---
D Flip Flop Details
A D flip flop captures the D data input pin value at the rising edge of the clock and hold that captured value at the Q output until the next rising edge
For best design practices, ONLY use flip flops that capture the D input on the rising edge of the clock
Flip Flops can be design to also capture data on the falling edge of the clock but it NOT a good design practice to mix rising and falling edge flop flops together in a system. This is because it is very difficult to control the duty cycle of the clock to 50% high 50% low and thus the timing between clock edges is difficult to predict
The D Flip Flop physics require a window around the rising edge of the clock were the D input cannot change
This window is the setup time, time before the rising edge, and the hold time, the time following the rising edge
If the D input changes in this window the Flip Flop will go to an unstable state called metastable and the output is unpredictable
If the timing to the D input cannot be met the system is failing to meet the timing requirements and will need redesigned

---
Register Logic
So in summary, the register logic is the data storage device that captures the state of the logic values at the rising edge of the clock
The clock is the system synchronous rate control and set the rate at which events are captured
RTL is an event driven language were the registers capture the events at the specified clock rate
The registers are analogous to independent threads that are updated atomically at the rising edge of the clock
The physics of the system dictates that the clock rate cannot exceed the data path delay from the flip flop output, through the functional logic, and back into the D input of the flip flop(s)
The data path to the flip flops cannot exceed the period of the clock minus the D input setup time

---
Combination Logic
While the register logic is the capture and storage of the data values at the clock rate, combination logic is the functional logic of the system that define the system operations
Combination logic is asynchronous and is not event driven by the clock
Combinational logic has only a physical delay from the variable inputs to the logic output that is a function of the number of level of operations
The logical operation performed by the combination logic is defined from a sum-of-products
The sum-of-products are the AND(s) and OR(s) of the variables to produce a specific logic output
Before the advent of HDL such as Verilog, sum-of-products were reduced using Karnaugh Maps
HDL eliminates the need for hand logic reductions
The reduction of very complex functions to a sum-of-products is greatly simplified using HDL

---
Logic Cone
A sum-of-products logic structure is also commonly refereed to as a logic cone
This is due to the funnel nature of the reduction of many variable inputs down to a single output
Since each logic cell has an insertion delay from the input to the output, the deeper the logic cone the larger the insertion delay
The concept of viewing the sum-of-products as a logic cone helps to understand the importance of controlling the combination logic delay to close timing
Controlling the depth of the logic cone will set the maximum frequency that the system can operate

---
Combination + Synchronous = System
A complete system is the merging of the synchronous register logic with the combinational logic
The register logic will hold the present state of the system and will update atomically at the next rising edge of the clock
The combination logic will calculate the next state of the system asynchronously following the rising edge of the clock and the update of the system state values
An Example design is a 3 bit counter as shown in the following truth table
The Q output of the registers represent the present state of the counter
The D input of the counter is the next state value of the counter
The logic to calculate the D input values from the Q output values is done by the combinational logic portion of the design that is a reduced sum-of-products
The complete insertion delay from the Q output to the D input plus the setup time required by the D input will set the maximum frequency the counter can operate
Thus the larger the counter gets the deeper the logic cone from Q outputs to D inputs becomes and the slow the operating clock rate
Present State			Next State
Q0	Q1	Q2	D0	D1	D2
0	0	0	0	0	1
0	0	1	0	1	0
0	1	0	0	1	1
0	1	1	1	0	0
1	0	0	1	0	1
1	0	1	1	1	0
1	1	0	1	1	1

---
Hierarchy Design
One more concept to review before we start looking at HDL coding is the concept of hierarchy design
As with all engineering problem solving, it is best to first reduce the complex problem into more manageable problems that can be assigned to multiple members of an engineering team
A hierarchy block is a section of the design that has a set of input and output signals
There are no limits to the levels of hierarchy and the number of input/output signals
The same block can be instantiated multiple times
All blocks of the core design are assembled up to the top level of the design were the input and outputs of the device are instantiated

---
HDL Block Outline
The following is a default format that can be used for all Verilog files
A template for this format is recommended
Module
Define the input and outputs of the hierarchy block
The best practice is to use only input and outputs in the core logic of the design
Internal Signal Definitions
Two internal signal types
reg – internal register variables that are assigned in always statements
wire – internal connection signals that are assigned outside an always statement
Note that module level output signals are by default also wires
Synchronous register definition
This is an always block that has a sensitivity list of the edges of the clock and reset signals
This block will generate the flip flop register of the design
All assignments in this always statement must use the non-blocking assignment <=
Any register outputs that are assigned to output signals from the module section can be assigned to the output signals following the register always block
Some designers will use repeat always statements for registers through the code but this can make the code become spaghetti. For a good synchronous single clock system one only needs one always statement for the registers and once for the combination logic
Asynchronous logic definition
This always block is the combination assignments that calculates the next state of the register values
All assignments in this always block are blocking assignments =

---
Sample Counter
This is a sample Verilog code for a counter
The counter is an 8 bit up or down counter
The counter has an asynchronous reset to zero
A control input signal is used to synchronously reset the counter to zero
A control input signal is used to set the up or down count direction
A control input signal is used to enable the counter or to hold the count
The present count value is an output
A signal output indicates when the counter goes from 15 to 16
A signal output indicates when the counter goes from 33 to 32
A signal output indicates when the counter rolls over back to zero
A signal output indicates when the counter under runs from zero back to 255

---
Module
module counter //{
    (
        //--------------------------------------------------------------------
        // clock and reset
        //--------------------------------------------------------------------
        i_clk, // clock input
        i_rst_n, // low asserted reset input
        i_srst, // synchronous reset input
        //--------------------------------------------------------------------
        // Counter control inputs
        //--------------------------------------------------------------------
        i_cnt_enable, // enables the counter when high and holds when low
        i_cnt_up_dw_n, // count up when high and down when low
        //--------------------------------------------------------------------
        // Counter output signals
        //--------------------------------------------------------------------
        o_cnt_value, // Counter output value
        o_cnt_15_16, // counter output went from 15 to 16
        o_cnt_33_32, // counter output went from 33 to 32
        o_cnt_ro, // roll over from 255 to 0
        o_cnt_ur // underrun from 0 to 255
    ); // End of Module }
    // Port Declarations {
        //--------------------------------------------------------------------
        // clock and reset
        //--------------------------------------------------------------------
input i_clk;
input i_rst_n;
input i_srst;
        //--------------------------------------------------------------------
        // Counter control inputs
        //--------------------------------------------------------------------
input i_cnt_enable; // enables the counter when high and holds when low
input i_cnt_up_dw_n; // count up when high and down when low
        //--------------------------------------------------------------------
        // Counter output signals
        //--------------------------------------------------------------------
output[7:0] o_cnt_value; // Counter output value
output o_cnt_15_16; // counter output went from 15 to 16
output o_cnt_33_32; // counter output went from 33 to 32
output o_cnt_ro; // roll over from 255 to 0
output o_cnt_ur; // underrun from 0 to 255
Note that the input signals are i_* and outputs are o_*. This is a good naming convention that allows others to easily see that the signals are the top level IO signals of the block when simulating or simply reading the code
The input and output definitions are outside of the module statement but could be in the module statement as defined in Verilog 2001 updates to the standard
Note that the o_cnt_value output is defined as an 8 bit bus [7:0]
Signals that are low asserted, like the async reset i_rst_n, end in _n to indicate the assertion level
Note that the i_cnt_up_dw_n counts up on high and down on low

---
Internal Signals
    // Internal Signal Declarations {
reg[7:0] q_cnt_value; // Counter output value
reg[7:0] d_cnt_value; // Counter output value
reg q_cnt_15_16; // counter output went from 15 to 16
reg d_cnt_15_16; // counter output went from 15 to 16
reg q_cnt_33_32; // counter output went from 33 to 32
reg d_cnt_33_32; // counter output went from 33 to 32
reg q_cnt_ro; // roll over from 255 to 0
reg d_cnt_ro; // roll over from 255 to 0
reg q_cnt_ur; // underrun from 0 to 255
reg d_cnt_ur; // underrun from 0 to 255
    // End of Internal Signal Declarations }
The internal signals for this block are the registers of the system and the next state values
The q_* signals are the present state values of the system. This is the Q output of the flip flops. This system has 8 registers for the counter and single flip flops for the output states of the system
The d_* signals are the next state values of the system and these signals are the combination logic cones of the system. These signals go the D input of the flip flops
The q_* and d_* make the code more readable and easier to sort the registers and next state values in the simulator. The naming convention also makes it easier to sort out the flip flops of the system once synthesized to gates which will be explained in later lessons

---
Synchronous Registers
Note that a task is used to define the reset values of the flip flops. This is because the async and sync reset states are the same so a task is used to define the same state for either reset
Also note the resets are assigned a default 0 value. Verilog will handle the casting of the values to the proper bit width
The always statement has a sensitivity list of posedge i_clk or negedge i_rst_n. This means that this always statement will only run on either of these two conditions
If the always statement executes and the i_rst_n is low then the reset task is called. This is the async reset
If the positive edge of the clock occurs and then async reset is high, then if the sync reset is asserted the reset task is executed, otherwise the present state of the flip flops q_* are updated to the next state values d_*
Note that all the assignments in the always statement are non-blocking <=
Finally outside the always statement, the flip flop present states are assigned to the output wires using the assign statement
// Reset Task {
task regrst;
    begin
        q_cnt_value <= 0;
        q_cnt_15_16 <= 0;
        q_cnt_33_32 <= 0;
        q_cnt_ro <= 0;
        q_cnt_ur <= 0;
    end
endtask
// End Reset Tast }
// Synchronous Registers {
always @(
        posedge i_clk or
        negedge i_rst_n
)
begin
    if (!i_rst_n)
        begin
        regrst();
        end
    else if (i_srst)
        begin
        regrst();
        end
    else
        begin
        q_cnt_value <= d_cnt_value;
        q_cnt_15_16 <= d_cnt_15_16;
        q_cnt_33_32 <= d_cnt_33_32;
        q_cnt_ro <= d_cnt_ro;
        q_cnt_ur <= d_cnt_ur;
        end
end // End Synchronous Registers }
assign o_cnt_value = q_cnt_value;
assign o_cnt_15_16 = q_cnt_15_16;
assign o_cnt_33_32 = q_cnt_33_32;
assign o_cnt_ro = q_cnt_ro;
assign o_cnt_ur = q_cnt_ur;

---
Combination Logic
Note that the always statement is conditional on the (.*) This is a short hand that means that the list of conditions are automatically determined
The first assignments are to set the next state values to some default value. This is very important and required to prevent the generation of latches. Latches are similar to flip flops but are not updated by the clock edge but transparent when the clock is asserted. Latches are not a good design practice and need to be avoided. A latch will be generated in this always statement if an if or case statement is not completely assigned like an if without an else
Note that in this block all assignments are blocking = This means the code executes from top to bottom so the d_* signals in the status output section are the updated values from the counter values assignments make just above the status assignments
Note that the if assignments are similar to C code excepted for the begin/end instead of {/}
// Next State Process {
always @(*)
begin
    // default values to prevent the generation of latches
    d_cnt_value = q_cnt_value;
    d_cnt_15_16 = 0;
    d_cnt_33_32 = 0;
    d_cnt_ro = 0;
    d_cnt_ur = 0;
    // set the counter values when enabled
    if(i_cnt_enable)
    begin
        if(i_cnt_up_dw_n)
        d_cnt_value = q_cnt_value + 1;
        else
        d_cnt_value = q_cnt_value - 1;
    end
    // find status outputs
    if((d_cnt_value == 16) & (q_cnt_value == 15))
        d_cnt_15_16 = 1;
    if((d_cnt_value == 32) & (q_cnt_value == 33))
        d_cnt_33_32 = 1;
    if((d_cnt_value == 0) & (q_cnt_value == 255))
        d_cnt_ro = 1;
    if((d_cnt_value == 255) & (q_cnt_value == 0))
        d_cnt_ur = 1;
end // End Next State Process }